Beijing University of Posts and Telecommunications
北京邮电大学
CONTROL BOARD FOR CNC SYSTEMS BASED IN LINUX
Author: Rodolfo Boris Oporto Quisbert
Final Project

---
Contents
- 1 Introduction
- 2 Background and technologies
- 3 Design and implementation
- 4 Results
- 5 Conclusions and future work

---
1 Introduction
- Project motivation
  - Try to make a fully functional control board for CNC systems.
    - In the last years, this systems have attracted the attention of many groups, interested especially in 3D printers.
  - Research about Open Source solutions a its characteristics.
    - Raspberry-Pi, LinuxCNC, Xenomai, RepRap, Raspbian.

---
2 Background
- Raspberry Pi
  - Raspberry-Pi is a low cost fully-functional computer, based in BCM2835 SoC from Broadcom.
  - This board was developed to be used as part of an educational program in UK.

---
2 Background
- Raspberry Pi
  - Low cost (~300RMB)
  - Huge community.
    - Support.
    - Docummentation.
      - Blogs, papers, internet forums, books.

---
2 Background
- Real time under Linux
  - PREEMPT_RT patch
    - Preemption: Preemption is the interruption of a computer process without its cooperation
    - How does it work?
      - Making in-kernel locking-primitives.
      - Critical sections protected.
      - Implementing priority.

---
2 Background
- Real time under Linux
  - Xenomai
    - Xenomai is a real-time development framework cooperating with the Linux kernel.
    - API skins: native, POXIS, RTDM, pSOS
    - Two spaces
      - Kernel space: Hard real-time applications
      - User space: Real-time applications

---
2 Background
- Real time under Linux
  - Why Xenomai?
    - Xenomai has a well documented API with different skins.
      - Examples, internet forums, API html documentation.
    - There is experiences with Xenomai running in Raspberry-Pi and LinuxCNC.
    - Official Xenomai patch for Raspberry-Pi.

---
2 Background
- LinuxCNC
  - Software collection for CNC machines. Former know as EMC.
  - Hardware Abstraction Layer
    - LinuxCNC use software components know as Hardware Abstraction Layer (HAL)
    - The developer can abstract from the details inside these blocks and use it like Symulink block.

---
2 Background
- LinuxCNC
  - Hardware Abstraction Layer
    - Some very important HAL components
      - RT Threads: hard real time thread which can be used to perform HAL functions at specific time
      - Stepgen: This component allow to control stepper-motors, generating all the signals required.
      - PID: This component implements a PID control block.
      - PWMgen: This component generate a PWM signal.

---
2 Background
- RepRap - 3D printer
  - RepRap is an Open Source project which starts in 2005, in the University of Bath, in UK by Adrian Bowyer. The aim of RepRap project was to create a 3D printer cheaper than the commercial ones, and the most important, a self-replicant 3D printer.

---
3 Design and implementation
- Board description
  - ADC: The core of the ADC system is the ADS8556 from Texas Instruments. This device has six channels, 16 bit's resolution, fully bipolar inputs, with serial or parallel communication. This device use SAR as conversion method. And the communication is through SPI.

---
3 Design and implementation
- Board description
  - ADC
    - Sample and hold subcircuit.
    - Voltage reference for resistive transductors

---
3 Design and implementation
- Board description
  - PWM: In this work was required N-MOSFET IRF630B to supply enough energy to components such as heaters and servomotors.

---
3 Design and implementation
- Board description
  - Steppers drivers: To control the stepper-motors, we use the A4983. A4983 is an integrated driver that just require the STEP and DIR signals.

---
3 Design and implementation
- Board description
  - MCP23S17 from Microchip.
    - 16 bidirectional I/O.
    - Control by interruption.
    - SPI communication.

---
3 Design and implementation
- HAL Driver
  - HAL is the highest level of a component in LinuxCNC. It means that any complex system is composed by several HAL blocks.
  - In this work was implemented a HAL component that controls the board.

---
4 Results
- Latency test
  - This test start two real-time threads and perform testing real-time functions.
  - The user interface present the average of latency in both, and the most important the maximum jitter value that can be interpreted as the minimum period that can be used to execute real-time functions.

---
4 Results
- Board tests
  - ADC test
    - samples_cvs.c
  - PWM test
    - pwm_test in LinuxCNC

---
4 Results

---
4 Results

---
5 Conclusions and future work
- Conclusions and results discussion
  - In general, the board designed, achieved a good integration with others blocks.
  - We found some speed lilmitations due to the maximum jitter provided by Raspberry-Pi
    - PWM maximum frequency 200Hz.
    - Maximum stepps 200 steps/second.
    - ADC maximum input signal frequency 10kHz
- Future work